## Slide 1
THERMAL CELL / BENCHMARK REVIEW
熱RCモデル基盤
9枚で読む設計・実装・検証
半導体装置の温度予測と状態監視を、保存則と外部ベンチマークで評価
thermal-cell-practical
Q̇
C Ṫ = −L T + b
y = H T + β
2026-09-28
Notes: Primary sources: docs/technical_specification.md; benchmarks/topcell/README.md.
The visual language follows the prior project deck. Tokyo Electron public IR material was used only as a color and layout reference. No logo or official template is included.
All benchmark values in this deck come from repository outputs regenerated or recorded on 2026-09-28.

## Slide 2
BACKGROUND
課題背景：高忠実度、疎観測、制御周期の時間差
温度場を保存則付きの少数状態へ圧縮し、設計と運転の判断を同じ状態定義で接続する
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
2
(a)
装置内の熱経路と観測
plasma
heat
chip / wafer
stage / base
coolant
q̇rad / q̇conv
T₁
T₂
T₃
局所センサだけでは内部温度、遅れ、未知発熱を直接観測できない
(b)
判断に使う時間尺度
1–2 s
monitor更新
因果的な状態・bias更新
180–600 s
過渡recipe
forecast / fault event
492–3,950 s
局所mesh solve
定常2ケースの実績
共通の低次元状態
CAE・実測を同じ熱収支へ写像し、予測と監視へ渡す
第三者が確認すべき問い
温度予測
未学習recipeでも誤差が増えないか
異常診断
sensorずれと実発熱を分離できるか
物理妥当性
mesh・放射・hotspot差を隠していないか
Notes: Sources: docs/product_architecture.md sections 1 and 10; docs/technical_specification.md sections 1, 4, and 9.
Monitor and benchmark sampling intervals are taken from TopCell and COMSOL published datasets.
Local-mesh solver times are from external_tools/comsol_chip_cooling/reports/cae_benchmark_report/source_data/mesh_convergence.csv.
The thermal-path diagram is a generic responsibility schematic, not a proprietary chamber cross section.

## Slide 3
CODE ARCHITECTURE
コードの処理構成
データ契約、物理engine、学習、推論を分離し、同じartifactをforecastとmonitorで共有する
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
3
OFFLINE 同定と検証
CSV / YAML
io/ config.py
契約検証
domain/
熱RC積分
engine/
robust同定
learning/
配備artifact
model.pt metadata.json
C Ṫ = −L(u)T + q(u) + Gᵦ[T∞(u) − T]
正値化した係数をcase-balanced Huber lossで同定
ONLINE 同じartifactを2つの因果workflowで使用
artifact
topology
係数・単位
schema / hash
forecast
history同化 | open-loop積分
将来温度・状態共分散・OOD
monitor
predict | innovation | update
物理状態・sensor bias・未知熱・NIS
責務境界
装置差は system.yaml と入力dataで表し、数値engineを装置名ごとに分岐しない
Notes: Sources: docs/product_architecture.md sections 2–10; docs/technical_specification.md sections 2, 6, 7, 8, and 10.
Implementation paths: src/celltemp/domain, engine, learning, workflows, artifact.py, inference.py, config.py.
The diagram follows the repository dependency direction: cli -> workflows -> learning/inference -> engine -> domain/io/config.

## Slide 4
BENCHMARK DESIGN
ベンチマークの問題設定
学習データと外部評価を物理的に分離し、汎化、観測可能性、故障帰属、model gapを別ケースで測る
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
4
(a)
4-node熱回路と観測式
T₁
CP
T₂
Center
T₃
middle
T₄
edge
G₁₂
G₂₃
G₃₄
heater
plasma
brine
y = H T + β + v
unknown heat d は既知source分布上で推定
(b)
学習と外部評価の境界
同定 228軌道
192 steady + 36 step/ramp
固定artifact
外部caseを学習探索から除外
12
forecast
未知level・波形・dt
5
monitor
noise・fault・欠測
1
model gap
非線形熱損失
評価軸
Generalization
RMSE / worst case / prior比較
Causality
未来観測なし / history handoff
Attribution
bias / unknown heat / NIS
Adequacy
意図的model gapを露出
単位：温度差 K、熱量 W、時間 s。forecastはopen-loop、monitorは因果更新。
Notes: Sources: benchmarks/topcell/docs/topcell_benchmark_problem.md; benchmarks/topcell/README.md; docs/units_and_conventions.md.
Training data comprises 192 steady trajectories and 36 independent step/ramp trajectories.
External evaluation contains 12 forecast cases and 5 monitor cases. F11 is the intentional model-gap case.
Synthetic criteria are software and workflow sanity thresholds, not product thermal limits.

## Slide 5
RESULT 1 / GENERALIZATION
外部11ケースは精度基準内、F11は構造不一致として分離
予測誤差は低いほど良い。negative controlのF11だけは高い誤差が正しい判定となる
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
5
(a)
予測精度と合格上限（低いほど良い）
Chart: RMSE [K]
| 11-case mean | worst case F09 sparse init
result | 0.14291 | 1.3027
acceptance limit | 1 | 1.5
(b)
学習効果とmodel-gap検出
Chart: RMSE [K]
| engineering prior | fitted core mean | gap detection floor | F11 model gap
RMSE | 7.185 | 0.14291 | 0.5 | 9.8234
PASS
平均 0.143 K / 上限 1.000 K
PASS
worst 1.303 K / 上限 1.500 K
PASS
F11 9.823 K / 検出下限 0.500 K
学習前から 98.0% 改善
model gapは下限の 19.6倍
Notes: Source: benchmarks/topcell/work/outputs/benchmark/benchmark_summary.json.
Source: benchmarks/topcell/work/outputs/benchmark/forecast_by_group.csv and forecast_by_case.csv.
The benchmark was rerun on 2026-09-28 with: uv run --locked --with-editable . python benchmarks/topcell/run.py.
Status=pass; core mean=0.142912 K; worst=1.302677 K; prior mean=7.185014 K.
F11 is intentionally excluded from the 11-case core mean. Its large error is the expected evidence that the linear RC structure does not represent temperature-dependent heat loss.
No confidence intervals are shown because each bar is a deterministic case or case-group aggregate from one fixed benchmark definition.

## Slide 6
RESULT 2 / INITIALIZATION
20秒の因果履歴で同一評価窓RMSEを90.1%低減
同じ2センサでも、履歴を使うと未観測nodeの初期状態を熱結合から推定できる
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
6
(a)
観測条件
0 s
20 s
180 s
F09: t=0で2点観測
F12: Center / middle を20 s観測
open-loop forecast
(b)
履歴後の瞬時4-node RMSE（低いほど良い）
Chart: time [s]
| 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180
F09 t=0 sparse initialization | 1.5937 | 1.137 | 0.82206 | 0.60828 | 0.46592 | 0.37289 | 0.31255 | 0.27268 | 0.25769 | 0.23889 | 0.22163 | 0.20623 | 0.19241 | 0.17984 | 0.16831 | 0.13917 | 0.12945 | 0.1212 | 0.11296 | 0.10499 | 0.097513 | 0.09059 | 0.084234 | 0.078419 | 0.10453 | 0.10527 | 0.10138 | 0.095108 | 0.088537 | 0.082601 | 0.077454 | 0.072966 | 0.068971
F12 20 s causal history | 0.076629 | 0.063374 | 0.064226 | 0.063799 | 0.060307 | 0.05504 | 0.049249 | 0.043717 | 0.027786 | 0.022862 | 0.021071 | 0.01928 | 0.01743 | 0.015692 | 0.014118 | 0.029459 | 0.03173 | 0.031101 | 0.028565 | 0.025624 | 0.023029 | 0.020959 | 0.019344 | 0.018052 | 0.026005 | 0.045015 | 0.04862 | 0.044946 | 0.039186 | 0.033656 | 0.029124 | 0.025675 | 0.023151
(c)
一次判定 F12 / F09（低いほど良い）
Chart: ratio [%]
| actual | acceptance maximum
F12 / F09 | 2.9243 | 25
PASS
2.9% / 上限 25%
同一評価窓
F09 0.384 K F12 0.038 K 90.1%低減
一次指標
F09 1.303 K F12 0.038 K
Notes: Predictions: benchmarks/topcell/work/outputs/forecast/F09_sparse_initial_observation.csv and F12_history_initialized_sparse.csv.
Truth: benchmarks/topcell/work/data/eval/forecast/F09_sparse_initial_observation.csv and F12_history_initialized_sparse.csv.
Common-window RMSE from t=20 s through 180 s: F09=0.383745 K, F12=0.038094 K, reduction=90.073%.
Benchmark primary ratio F12/F09=2.924%; acceptance maximum=25.0%.
The benchmark primary metric compares the published F09 full-horizon score with the F12 origin-after-history score. The common-window calculation is added to make the comparison conservative and time-aligned.
The line plot is downsampled every 5 s for display only. RMSE values use all forecast rows.

## Slide 7
RESULT 3 / MONITORING
監視5ケースは全基準内、異常種別も正しく帰属
棒が100%より短ければ合格。単位の異なる指標を各受入上限で正規化して比較する
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
7
(a)
受入上限の使用率（100%未満で合格）
Chart: acceptance-limit utilization [%]
| M01 innovation 0.168 / 0.350 K | M02 bias RMSE 0.104 / 0.150 K | M03 detection 0.0 / 2.0 s | M04 missing RMSE 0.084 / 0.250 K | M05 detection 1.0 / 5.0 s | M05 heat RMSE 0.135 / 0.250 W
actual / limit | 47.864 | 69.2026 | 0 | 33.6855 | 20 | 54.0997
acceptance boundary | 100 | 100 | 100 | 100 | 100 | 100
(b)
帰属結果
M03 sensor step fault
PASS
0 sで検出
first alert: CP
peak NIS: 279.2
判定: sensor bias
M05 unmodeled heat
PASS
1 sで検出
peak estimate: 0.757 W
heat RMSE: 0.135 W
判定: physical disturbance
MONITOR 8 / 8 CHECKS PASS
故障検出だけでなく、センサ起因か熱負荷起因かを分離
Notes: Source: benchmarks/topcell/work/outputs/benchmark/monitor_by_case.csv.
Source: benchmarks/topcell/work/outputs/benchmark/benchmark_summary.json.
Acceptance-limit utilization equals the measured metric divided by its benchmark acceptance maximum. Lower is better and 100% is the boundary.
M03 localization is checked separately because first-alert sensor identity is categorical. M04 posterior finite-state behavior is also checked separately.
Monitor checks passed: 8/8.

## Slide 8
RESULT 4 / HIGH FIDELITY
平均温度はスクリーニング可能、放射感度は未再現
mesh、絶対温度、物理差分を別々に判定し、用途をvolume-average screeningへ限定する
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
8
(a)
medium−fine差と用途別上限（低いほど良い）
Chart: chip-average |ΔT| [K]
| MC01 nominal | MC02 hot + radiation
actual ¦ΔT¦ | 0.49621 | 0.15443
strict max | 0.25 | 0.25
benchmark max | 0.5 | 0.5
strict 1/2 pass
benchmark 2/2 pass
(b)
220秒時点の放射効果（絶対値）
Chart: chip |ΔT| [K]
| CAE truth | RC model
¦HV02 − HV01¦ | 0.38133 | 0.0012223
同じ冷却方向 大きさの再現率 0.3%
PASS
平均RMSE 0.096 K worst 0.144 K
CONDITIONAL
mesh strict 1/2 benchmark 2/2
FAIL
放射効果 0.001 / 0.381 K
判定境界：66点の平均温度screeningに使用可。hotspot、放射設計、interlockには使用不可。
Notes: Mesh source: external_tools/comsol_chip_cooling/reports/cae_benchmark_report/source_data/mesh_convergence.csv.
High-fidelity metrics: external_tools/comsol_chip_cooling/reports/cae_benchmark_report/source_data/high_fidelity_case_metrics.csv.
Radiation trace: external_tools/comsol_chip_cooling/reports/cae_benchmark_report/source_data/high_fidelity_radiation_trace.csv.
Validation boundary: external_tools/comsol_chip_cooling/docs/high_fidelity_validation.md.
Computed medium-to-fine chip-average differences: MC01=0.4962086 K, MC02=0.1544275 K.
At 220 s, CAE radiation-pair chip delta magnitude is 0.38133367 K and the RC-model magnitude is 0.00122234 K.
High-fidelity mean RMSE=0.09561862 K; worst=0.14358424 K; scalar predictions=66.
Interpretation: absolute average-temperature screening improved, but the magnitude of the radiation sensitivity is not validated.

## Slide 9
CONCLUSION
現時点の適用範囲と次の検証
保存則付きの高速推定層として有用。製品判断へ使う範囲は証拠の強さに合わせて限定する
THERMAL CELL / BENCHMARK REVIEW · 2026-09-28
9
証拠に基づく適用範囲
使用可能
TopCell予測・監視と線形CAE screening
外部11ケース精度基準内、monitor 8/8、線形COMSOL 10/10
条件付き
高忠実度のvolume-average screening
平均RMSE 0.096 K、benchmark mesh 2/2、strict mesh 1/2
未検証
放射感度、hotspot安全、interlock
放射効果の再現率 0.3%、時間刻み収束と実験比較は未実施
製品適用までのgate
01
離散化を収束
meshと時間刻みを用途基準へ収束
02
同一観測量で実験比較
領域平均と計測不確かさを対応
03
運用thresholdを固定
FMEA、誤警報率、thermal margin
結論
高忠実度CAEと実測の間に、物理整合した高速な予測・監視層を置ける
Notes: Sources: benchmarks/topcell/work/outputs/benchmark/benchmark_summary.json; external_tools/comsol_chip_cooling/work/evaluation/summary.json.
Sources: external_tools/comsol_chip_cooling/docs/high_fidelity_validation.md; docs/technical_specification.md sections 11 and 12.
Linear COMSOL external forecast mean RMSE is 0.036276 K and all 10 screening checks pass. This is volume-average screening evidence, not hotspot product acceptance.
Recommended product gates follow the repository validation boundary and should be tied to the equipment FMEA, control period, and thermal budget.